Hatchrite Corp.

999 Settings

Depress the “UP and “Down” Arrows simultaneously (About 3 seconds) until “In Red” we see the Abbreviation “INPT” At this point let go of these buttons. Now move to the “MODE” Button. Depress this button to step thru the input menu as shown below. Verify each setting and change any incorrect settings as needed by using the “UP” or “Down” arrows. As you step thru the “Temperature” Menu you will then automatically pass into the “Humidity” Portion of the “Input” Menu. After verifying these settings the menu will lead back to the beginning of our “Input” menu. This pattern will repeat itself after each portion of the menu verification. Now depress the “UP’ Arrow one time to get to the “OUTPUT” portion of the menu abbreviated “OTPT” Move to the “MODE” Button and step through each setting, verify each. At any time you feel you have erred, Depress the display button to get out of the menu and start over.

Note: under each menu heading there are parameters for temperature and Humidity. On the left of each of these columns the readout on the controller will be on the bottom (in Green). The right hand column will appear on the upper portion of the controller (in Red).

| Input Menu | Output Menu |
| --- | --- |
| TEMP | HUMD | TEMP | HUMD |
| In1 | 4-20 | In2 | 4-20 | Ot1 | Ht | Ot2 | Ht |
| deC1 | 0.0 | deC2 | 0.0 | HYS1 | 0.3 | HYS2 | 0.3 |
| rL1 | 60.0 | rL2 | 100.0 | OT1 | no | OT2 | No |
| rH1 | 111.2 | rH2 | 0.0 |  |  |  |  |
| CAL1 | 0.0 | CAL2 | 0 |  |  |  |  |
| Ftr1 | 0 | Ftr2 | NO |  |  |  |  |

| Global Menu | Comm Menu |
| --- | --- |
| Fail | bPL5 | bAUd | 4800 |
| Err | nLA | dAtA | 7o |
| Ei1 | No | Prot | On |
| Anum | On | IntF | 485 |
| Atsp | 90 |  |  |
| rP1 | OFF |  |  |
| rP2 | OFF |  |  |

The next portion of our Watlow Control settings pertains to the manner in which your machine reacts to the temperature and Humidity settings

Set points

These are called the P.I.D.’s.

To get to these settings depress the “MODE” Button one time. The abbreviation “SYS” will appear. Depress the “UP” Arrow one time. The Menu heading P.I.D. “A” will appear. At this depress the “MODE” button as we did in the previous menu. Verify each setting and correct as needed.

As we pass through each setting using the “MODE” Button we will again arrive back to the P.I.D. “A” Heading. Depress the “UP Arrow once again to arrive at the P.I.D. “B” Menu. Depress the Mode button to step through these settings

| P.I.D. “A” | P.I.D. “B” |
| --- | --- |
| Pb1A | 1.5 | Pb1B | 2.4 |
| rE1A | .12 | rE1B | .46 |
| rA1A | .75 | rA1B | .08 |
| Ct1A | 1.0 | Ct1B | 1.0 |

If you do not have our computer controlled version it will be necessary to access our roll interval and roll time. These Machines will be designated as “CP”

To Access these features depress the “MODE” button two times. At this point you will see in the lower readout “rl”. It is recommended that this setting be the numeral “One” (1). This will set the machine to roll once every hour. To set the roll time (The amount of time the machine rolls) you depress the “MODE” button once more. In the lower read-out you will see “rt” the upper read-out will show our roll time in seconds. The table below will give you start points for the roll time settings.

| Emu | Ostrich | Rhea |
| --- | --- | --- |
| 18 seconds | 24 seconds | 18 seconds |

These values will vary depending on egg size and are approximations only.